FHGD:APPLIED FUZZY HEURISTICS FOR GREEDY NODE DETECTION IN VANETs
MR.X	Mrs.R.VENITTA RAJ
    M.ANUPRIYA,P.POOJA,K.DHIVYABARATHI
Abstract-The  Vehicular Ad hoc Network(VANETs) has a greater significance in Vehicle to Vehicle Communication without relaying much on the Infrastructure.Though they are used in variety of applications they are vulnerable to attacks.In this proposed approach we have to detect greedy nodes  by incorporating various various metrics like Number of times the node makes an Attempt, Connection Duration , Waiting time, Packet Delivery Ratio and Average Delay. These metrics are used by the benign nodes to learn more about malicious node behavior.In order to detect greedy nodes our proposed model has two phases namely Uncertainty  State and Resolution State .The Uncertainty  State is based on linear regression concept and Resolution state is based on Fuzzy Logic Scheme.The effectiveness of our approach is proved by extensive simulations. This proposed work can be applicable for variety of applications as they provide high level of trustworthiness by detecting greedy nodes in the network.
1.INTRODUCTION:The main use of Mobile Network in VANETs is in adhoc mode.The algorithm work is to detect greedy node and safeguard the life of the passengers from the attacks[1].compare to VANETs,MANETS have less constraint.
The VANETs proposal ensures privacy for the driver and his vehicle wheather he is tramitter or receiver of the message.By handling vehicular behaviour during traffic,we ensure a safe and secure traffic management.In the proposed model we define a three newly defined metrices
A mobile ad hoc network is a collection of two or more nodes equipped with Wireless communications and networking capabilities without central network control,which may be referred to as an infrastructure-less mobile network.
Vehicular Ad-hoc Networks(VANETs)represent a rapidly emerging,particularly challenging class of Mobile Ad Hoc Networks(MANETs).VANETs are distributed,self organing communication networks bulit up by moving vehicles and thus characterized by very high node mobility and limited degrees of freedom in the mobility patterns.
In ad hoc networks all nodes are mobile and can be connected dynamically in an arbitrary manner.As the range of each host’s Wireless transmission is limited,so a host needs to enlist the aid of its nearby hosts in forwarding packets to the destination if it wants to communicate with the hosts outside its transmission range.so the nodes of the networks behave as routers and take part in route discovery and maintence of routers to other nodes in the network.
 In[2] the attack against VANETs are of availability,integrity etc.availability of attacks are of denial of service (DoS)attack[3].A DoS attack occurs when a multiple system orchestrate a synchronized Dos attack to a single target.Dos attacks are generally against large corporations,government sites to distrupt their web prescence.In vanets the detection of DoS is little difficult.The greedy node job is to reduce the faster time of the channels and to disturbs the other honest node.The greedy node is that disobedience that is not to work with the honest node.
   The performance of MAC layer be affected in the manner of the backoff value.The contention window of the subrange be specified by receiver to sender through CTS/ACK packet.the contention window is easy to detect misbehaving nodes. The RTS/CTS(Request to send/clear to send)is the mechanishm for wireless network protocol to reduce the collision by the hidden node problem. The Distributed short range communication(DSRC) is open source protocol for wireless communication.The featured of DSRC is of high secure and high speed and is of wireless communication between vehicles and infrastructure.The DSRC is classified into 7 channels of 10 MHZ:one CCH channel (Control channel)and six SCH channel(service channel) .VANETs introduced WAVE(Wireless access in vehicular environments) WAVE includes the data exchange between high-speed vehicles and the roadside infrastructure is relied on the band of 5.9 GHz(5.85-5.925 GHz).WAVE is required to support the Intelligent Transportation System(ITS) in short range application.
The contention based method called Enhanced Distributed Channel Access(EDCA) is considered as mandatory mode for Medium Access Control(MAC).EDCA features such as Arbitration Inter –Frame Space(AIFS)and contention window for different access categories(AC) .four categories are classified according to the type of traffic:Background traffic(BK),Best Effort Traffic(BE),Video traffic(VI),Voice traffic(vo).
Time=15us,SIFS=32us represent the Short Inter Frame Space for IEEE 802.11.
CCH	SCH

AC CWmin CWmax CWmin CWmax

BK min max min max
BE (min+1)/2 min min max
VI (min+1/4)-1 min+1/2 min+1/2 min
VO (min+1/4)-1 min+1/2 (min+1/4)-1 min+1/2

Min=15 Max =511
The EDCA uses access channel method as CSMA/CA(Carrier Sense Multiple Access with collision Avoidence).The backoff procedure follows the backoff value[0,CW] equal to initial value CWmin,if the CW fails to reaches CWmax then the CW increases,when channel is idle the backoff value reduced,the node send immedieately it the value reaches zero.
     =*time (1)
Different AIFSN(arbitration inter frame space number)are been selected on the basis of access categories for use with CCH and SCH for control and service channels.the detection of greedy node be understand on the basis of CWmax,CWmin and AIFSN values.
2.MANET ARCHITECTURE AND CHARACTERISTICS:
1.Dynamic topologies:
In MANET nodes are free to move readily,thus network topology which it act as a multihop may change suddenly at unpredictable times,and consist of both bidirectional and unidirectional links.
2.Bandwidth-constrained,variable capacity links:
Wireless links have significantly lower capacity than hardwired counterparts.one effect of the relatively low to moderate link capacities is that congestion is typically the norm rather than expectation.

3.Energy-constrained operation:
The nodes in a MANET may rely on batteries or other exhaustible means for their energy.The most important system design criteria for optimization may be energy conservation for these nodes.
4.Limited physical security:
Mobile Wireless networks are generally more prone to physical security threats than the infrastructure based networks.The increased possibility of eavesdropping,spoofing and denial-of-service attacks shoud be considered.This provides the decentralized nature of network control in MANETs to be robust against the single points of the failure of more centralized approaches.
3.RELATED WORK:
       The problem in this paper are we have to detect the dos attacks,MAC layer misbehaviour and also to detect the greedy behaviour .The approaches mainly focus on the VANETs on the IEEE802.11 protocol.In that we have proposed for Mac greedy behaviour detection in Wireless Mesh Networks(WMNs).There be classified as Three series
- Mac Design Solutions:To reduce Back off algorithm weekness.A new Mac layer is introduced to detect the greedy attacks.
- Monitoring solutions:Without modification of the MAC layer an extra component is added to detect greedy attacks.
- Game theory solutions:the detection of greedy attacks be based on the game theory approach.
DOMINO was Proposed by Raya et al.[6](System for greedy behaviour in the MAC layer of IEEE 802.11 public Networks).DOMINO can detect and identify greedy attacks without any modification of the access point.It can detect some manipulation techniques such as CTS and ACK delay and reduction of Backoff time.
Confident was proposed by Buchegger and Le Boudec it is been mainly used in Mobile ad-hoc networks and it works properly on the participating nodes cooperate in routing and forwarding.CONFIDENT for making misbehaviour unattractive to deny cooperation.
login attempts,connection duration,connection waiting time

Djahel et al proposed a FLASC(fuzzy logic based scheme to struggle against adaptive cheaters).The main objective of FLASC is to detect greddy nodes which aim to violate proper use of CSMA/CA protocol.
In VANETs regular changes in private communication pseudonyms are important to avoid illegal tracking of vehicles and to ensure anonymity.Pseudonym change protocol based on the detection of trusted neighbours.This protocol triggers the pseudonym change in several vehicles at the same time ,a solution that improves vehicles anonymity.
The security protocol based on the dyanamic change of pseudonyms for privacy in Vehicular Ad hoc networks(VANETs).The privacy for the driver and his vehicles wheather he is transmitter or receiver of the messages.
3 PROPOSED DETECTION ALGORITHM
3.1 Algorithm Overview
The watchdog software determines the responsible for greedy behaviour detection for three defined metrices. we have queue length,throughtput,packet delivary ratio.

Calculate slope of regression of straight line

Close to 1

        Coefficient calculation

        Collection of traces

Close to 1
Greedy behaviour Unsavoury State

No greedy behaviour

Greedy determination(yes/no)

These metrices are responsible for low mobility networks.In VANETs there is no enough time to perform the detection of greedy behaviour backoff parameters.the number of connection attempts,connection duration and waiting time are supervised.so that in this project combines linear regression and Watch dog concepts for the VANETs.The decision scheme uses strength of design tools by the fuzzy logic to determine either greedy or it is honest.

Unsavoury State :In Unsavoury State phase,we determining wheather our network contains any greedy node or not .In 802.11p architecture, if the first node communicate with other node,next node will be wait till first node break its transmission. Now first create the number of node in network with fixed coordinates.Then generate the trace file. Using this coordinates find the correlation coefficient. we calculate the correlation coefficient means a number between +1 and -1 calculated so as to represent the linear interdependence of two variables or set of data. If correlation coefficient is nearer to 1 means we must calculate slope of linear regression line .If slope also nearer to 1 means greedy node is not present in this network.Otherwise greedy is may or may not be present.So that finding the exact result we use watchdog tool.

Algorithm 1. Greedy Unsavoury State :

INPUT	:Greedy=false.	OUTPUT:Network contains Greedy or not	begin	repeat	1)Collect coordinates	of nodes	2)Calculate the coefficient P	if P is nearer to 1 then	execute step 3.	Else execute step 4.	3)Calculate slope	if the slope is nearer to 1	Greedy=false;	Else execute step 4.	4)Greedy is Suspected .run	watchdog tool	until No communication;	end

Resolution State:
In this state,we using the fuzzy concept for finding the existence of greedy node.For each parameter we start to find the behavior of the node as Greedy,Suspected,Normal using the threshold value.Before doing that we should know about fuzzy concept. In our software tool monitoring the three parameter.	1)Number of Connection Attempt	2)Average of Connection Duration	3)Average of waiting time.

Fuzzy Concept:
In fuzzy concept,it contains the 3 phase.	1)Fuzzification(using membership function).	2)Rule Generation(Application of fuzzy rule)	3)Defuzzification(Obtaining the crisp or actual values).
Fuzzification:
Here,we use three parameter which is monitor by the watchdog tool as linguistic variable.For each value of linguistic variable,we fix its membership to one of the following fuzzy sets “low”,”high”,”medium”.Output of the membership should be between -1 and +1.
Description of the Parameter

Parameter	Description

n	No:of node	C	No:of Connection attempt at t. C	Connection duration during t. C1 size 12{ {} rSub { size 8{ ital "att"} } } {}	low threshold value of	connection attempt.	C2 size 12{ {} rSub { size 8{ ital "att"} } } {}	high threshold value of	connection attempt .	C1 size 12{ {} rSub { size 8{Δt} } } {}	low threshold value of	connection duration.	C2 size 12{ {} rSub { size 8{Δt} } } {}	high threshold value of	conncetion duration.	C1 size 12{ {} rSub { size 8{ ital "delay"} } } {}	high threshold value of waiting	time.	C2 size 12{ {} rSub { size 8{ ital "delay"} } } {}	low threshold value of	waiting time
Rule Generation:
Here,For each parameter we generate the rule using the threshold value.	size 12{C1 rSub { size 8{ ital "att"} } = { {"C " rSub { size 8{"att"} } } over {n} } } {} :low threshold value.if node exceeds this value,node is suspected.	size 12{C2 rSub { size 8{ ital "att"} } =0 "." 7C rSub { size 8{ ital "att"} } } {} high threshold value.if node exceeds this value,node is greedy.	size 12{C1 rSub { size 8{Δt} } = { {C rSub { size 8{Δt} } } over {n} } } {} :low threshold value.if node exceeds this value,node is suspected.	size 12{ ital "TH"2 ital "cd"=0 "." 6 ital "tcd"} {} :high threshold value.if node exceeds this value,node is greedy.	size 12{ ital "TH"1 ital "wt"="min" \( ital "AIFS" \) } {} low threshold vaue.if node being this value,node is greedy. size 12{C rSub { size 8{ ital "delay"} } ="max" \( ital "AIFS"+ ital "CW""max*"t \) } {} :high threshold value.if node being this value,node is suspected. P1Number of connection attempts	P2Connection duration	P3Waiting time

llow	hhigh	mmedium Nnormal	Ssuspected	Ggreedy
Fuzzy rules1:C1
If P1L AND P2L THEN node is L1	If P1L AND P2M THEN node is L1	If P1L AND P2H THEN node is M1	If P1M AND P2L THEN node is L1 If P1M AND P2M THEN node is M1	If P1M AND P2H THEN node is H1	If P1H AND P2L THEN node is M1 If P1H AND P2M THEN node is M1	If P1H AND P2H THEN node is H1
Fuzzy rule2:Class2
If C1L1 AND P3L THEN node is L1	If C1L1 AND P3M THEN node is L1	If C1L1 AND P3H THEN node is M1	If C1M1 AND P3L THEN node is M1 If C1M1 AND P3M THEN node is M1	If C1M1 AND P3H THEN node is H1	If C1H1 AND P3L THEN node is H1 If C1H1 AND P3M THEN node is H1	If C1H1 AND P3H THEN node is H1
size 12{ ital "PDR"= { {N} over { ital "seq" rSub { size 8{ ital "current"} } - ital "seq" rSub { size 8{ ital "prev"} } } } } {} --------------------3 size 12{ ital "AD"= { { Sum cSub { size 8{j=1} } cSup { size 8{m} } {t rSub { size 8{ ital "ack"} } - \( t rSub { size 8{d} rSub { size 8{N} } } - t rSub { size 8{d} rSub { size 8{j} } } \) - t rSub { size 8{ ital "source"} } } } over {m "." ital "AD" rSub { size 8{"max"} } } } } {} --------4
In this proposed system we also find trust of path in network using PDR(Packet Delivery Ratio) and AD(Average Delay) is achieved by FUZZY concept .From algorithm 2 we get node is normal or suspected or greedy.

Rule:no	PDR	AD	Class2	Node State
1	high	low	L1	Normal
2	high	low	M1	Normal
3	high	low	H1	Suspect
4	high	high	L1	Normal
5	high	high	M1	Suspect
6	high	high	H1	Suspect
7	low	low	L1	Normal
8	low	low	M1	Suspect
9	low	low	H1	Suspect
10	low	high	L1	Suspect
11	low	high	M1	Greedy
12	low	high	H1	Greedy

Description:

N	node of node size 12{ ital "seq" rSub { size 8{ ital "curr"} } , ital "seq" rSub { size 8{ ital "prev"} } } {}	from trace file	size 12{t rSub { size 8{ ital "dest"} } } {}	time of receiving node size 12{t rSub { size 8{ ital "source"} } } {}	time of sending node size 12{t rSub { size 8{ ital "ack"} } } {}	time for	acknowledgement size 12{ ital "AD" rSub { size 8{"max"} } } {}	maximum tolerable	delay

4.EVALUATION:
To find the greedy node in the network, we should evaluate the Unsavoury State and Resolution state . For getting more accurate result, we must calculate the Packet Deliver Ratio and Average Delay .Following diagram shows PDR and AD value changes depends on presence of greedy nodes in network.

Above data state that ,Efficiency of finding the greedy nodes in network.In existing system only use connection attempt ,waiting time ,connection duration.But in our propoed system we use PDR and AD value also.Compare than existing system our proposed system is got more accurate value.
REFERENCES:
[1] M.N.Mejri,j.Ben-Othman,and Hamdi,”Survey on VANET security Challenges and possible cryptographic solutions,”Vehicular common.,vol.1,pp.53-66,2014.	[2] A.Dhamgaye and N.Chavhan,”Survey on security challenges in VANET,” Int.j.comput.sci.,vol.2,pp.88-96,2013. [3] S.Zeadally,R. Hunt,Y.-S. Chen,A. Irwin,and A.Hassan,”Vehicular ad hoc networks(VANETs):status,results,and challenges,”Tellecommun.Syst.,vol.50,no.4,pp.217-241,2012. [4]M.N.Mejri and m. Hamdi,”Recent advances in cryptographic solutions for vehicular networks,”in proc.Int.symp.netw.comput.commun.,2015,pp.1-7.
[5]A.hamei,J.Ben-Othman,A.Gueroui,and F.Nait-Abedesselam,”Detecting greedy behaviours by linear regression in wireless ad networks,”in proc.IEEE Int.conf.commun.,2009,pp.1-6. [6]M.Raya,J.-P.Hubaux,and I. Aad.”Domino:A system to detect greedy behaviour in IEEE 802.11 hotspots,”in proc.2nd Int.conf.Mobile syst.appl.serv.,2004,pp.84-97. [7].DSRC,2013.[Online].Available: http://grouper.ieee.org/groups/scc32/dsrc/
[8] Yanbin Gao, Lianwu Guan, Tingjun Wang, Xiaodan Cong, "Research on the calibration of FOG based on AFSA", Mechatronics and Automation (ICMA) 2013 IEEE International Conference on, pp. 412-417, 2013.
[9]. N.K. Jha, Q. Tong, "Robustly testable static CMOS parity trees derived from binary decision diagrams", Solid-State Circuits IEEE Journal of, vol. 26, pp. 1728-1733, 1991, ISSN 0018-9200.
[10] Sharad C. Seth, K. L. Kodandapani, "Diagnosis of Faults in Linear Tree Networks", Computers IEEE Transactions on, vol. C-26, pp. 29-33, 1977, ISSN 0018-9340
[11] Fujiwara, "On Closedness and Test Complexity of Logic Circuits", Computers IEEE Transactions on, vol. C-30, pp. 556-562, 1981, ISSN 0018-9340.